## Slide 1: Analog Strain Gauge on a CAN Interface
Jack Glennon, Dylan Nektalov, Alex Swartz

## Slide 2: Project IDEA
Custom PCB to read analog strain gauge and transfer signals onto CAN bus
  Measure forces on GTMS vehicle aero and frame elements
MBED for demonstration
  Read CAN signals and display on PC terminal window
Parts
  ST microcontroller, NAU7802 AD converter, NCV7349 CAN Tx/Rx, MBED, SK Pang CAN breakout board, CMOS low dropout regulator, capacitors, LEDs, resistors, switches, pins

## Slide 3: Project Design
Strain Gauge
Analog to Digital Converter
ST Microcontroller
PCB
PC Serial Terminal
MBED
SK Pang CAN Breakout
Test Setup
120 Ω
CAN BUS
CAN Transceiver

## Slide 4: Software
MBED C++ to display messages
  CAN and SERIAL classes, ID filtering and masking, error handling
STM32 F042 (Cortex M0) for I2C, ADC, GPIO, Timing, and CAN function
  ST hardware abstraction layer (HAL)
  Custom ADC library
  Keil uVision for debugging and an ARM compiler
  Signal and power status LEDs through GPIO

## Slide 5: Demonstration

## Slide 6: Summary and Future Work
Demonstrated ability to generate and read CAN messages
Compact, durable PCB suitable for use in formula-style vehicle
Enables GTMS team to monitor and compensate for stresses
Investigate MBED functionality challenges and implement broader filtering
Create revised PCB with CAN IC standby selection pin routed to microcontroller
DIP switch for Boot0 pin to eliminate jumper
Silkscreen for analog in header